## Slide 1
Use GNU Octave to generate waves and check their outputs
Use .txt files as standard format for taking inputs
Thoroughly check and understand DAC requirements and specs, DAC sampling rate, frequency, bandwidth etc
Memory capacity to be finalized based on the input – considering floating point input
Waves can be in 3 phases : Equation based, Storage based, Arb (Blind values ie no reference )
Check what will be the full-scale output of DAC. This is a very important feature
A wave digitally is represented as discrete values of time ( sampling rate ) and discrete values of amplitude ( DAC )
Clock frequency output to user can be fixed. It need not be variable
Give the clock frequency output in the range of 1 MHz to 10 MHz
User inputs in the arb directly can be taken from the touch screen for standard wave forms
The noise requirement is AWGN – Arbitrary White Gaussian Noise – Study more on noise generation, check whether DAC support Noise generation, if so get the details
Bandwidth can be kept as 10MHz and for frequency values of less than 10 MHz take the bandwidth as 10% of the required output frequency. Bandwidth is a requirement for both Arb waves and for noise
Project Review dt 01.01.2025

## Slide 2
12. Study the specs of STM 32 446 and compare it with STM 32 401
13. Based on the memory capacity of STM you decide whether to retain floating point inputs or not
14. Duty cycle is an input that is required for generation of square waves. This input has to be taken from the user
15. Two channels are necessary as mentioned in the spec sheet
16. Elaborate the block diagram with finer details.
17. Study the kind of wave form that get generated by tweaking both frequency and amplitude of a sine wave formula and check the output in GNU Octave
18. Are you going to use USB as the the input for passing .txt files to STM ?
19. All the calculations for wave forms are wrt to time domain and not wrt frequency domain
20. Study the frequency domain of white noise
21. One cycle of a wave is what the user decides based on his type of wave form
22. Roles and responsibilities and timeline has to be elaborated and mention the details based on the project development headings.
Project Review dt 01.01.2025 cont…..